## Slide 1: Title
Low-Cost Controlled Lighting Setup
for Sub-mm Defect Detection

## Slide 2: Problem Statement
Goal:
Detect dents & scratches < 0.1 mm on phone surfaces
Key Challenge:
Lighting, not camera resolution

## Slide 3: Controlled Environment (Black Box)
• Light-sealed enclosure
• Matte black interior
• Dimensions: 45 x 45 x 40 cm
• Eliminates ambient light & reflections

## Slide 4: Object Placement
• Phone at center
• Height: ~6 cm
• Tilt: 5° towards camera
• Non-reflective holder

## Slide 5: Lighting Philosophy
• Lighting reveals defects via physics
• Shadows, reflections, gradients
• Multiple lights, one purpose each

## Slide 6: Lighting Layer 1: Top White Diffused
• 5500–6500K white LED
• Distance: 30 cm
• Fully diffused
• Used for reference, not defects

## Slide 7: Lighting Layer 2: Blue Raking Light
• 450–470 nm blue LED
• Angle: 25°
• Height: 4 cm
• Best for scratches & glossy surfaces

## Slide 8: Lighting Layer 3: Warm Raking Light
• 3000–3500K warm LED
• Angle: 10–15°
• Height: 2–3 cm
• Best for dents & depth

## Slide 9: Lighting vs Phone Color
Black / Glossy → Blue dominant
White / Matte → Warm dominant
Silver → Blue + Warm

## Slide 10: Photometric Stereo Concept
• Same camera, same object
• Change light direction
• Infer surface slope & depth

## Slide 11: Mathematical Insight
I = ρ (L · N)
Brightness change → Normal change
Normals → Slopes → Depth

## Slide 12: Pixel Requirement
For 0.1 mm defect:
Pixel size ≤ 0.02 mm
~3500 pixels across phone width

## Slide 13: Camera Recommendation
• Industrial USB camera (12 MP+)
• Macro lens
• Slight camera tilt (7°)

## Slide 14: Why This Works
• Lighting amplifies geometry
• Camera samples contrast
• Photometric stereo extracts shape

## Slide 15: Conclusion
Sub-mm defect detection is a lighting & geometry problem,
not a megapixel problem.